Electronics and Circuits
The Basics of an RL, RC, LC, and RLC circuit
Nikaansh Singh
02 August 2024

---
Electronics?
Study of the Flow of Electrons
Components
Devices
Systems

---
Circuit
Power Source
Interconnected path for Electricity
Provides the Energy
Load
Conductors
The Component that Consumes Electricity
Materials that allow the flow of Electricity
Control Element
Insulators
Controls the flow of electricity
Materials that don’t allow the flow of Electricity

---
Types of Circuits
Components are connected end to end
Components are connected across the same voltage source
Combination of both Series and Parallel
Series
Parallel
Combination

---
01 Ohm’s Law
02 Kirchhoff’s Voltage Law
V=IR
Voltage = Current * Resistance
Sum of all voltages in a closed loop is 0
03 Kirchhoff’s Current Law
Sum of all currents entering a junction is the same all the sum of all currents exiting the junction

---
01 Resistor
Limits the flow of the electric current.
Measured in ohms.
02 Capacitor
Stores energy in an electric field.
Measured in farads.
03 Inductor
Stores energy in a magnetic field.
Measured in henries.

---
Finding the Voltage
03 Capacitor
02 Inductor
01 Resistor
Using Ohm’s Law the Voltage across is resistor is
Where i is the current through the resistor and R is the resistance
Voltage of an Inductor is
Where L is the inductance and di/dt is the rage of change of current
Voltage of an Capacitor is
Where Q is the charge stored in it

---
How to Find Circuits as a Function of Time
Use KVL
Solve the Differential
All of these circuits are on a closed loop, meaning that we can use KVL to solve them
Since we are trying to find a time function, this is all done in respects to t, or time
Find Individual Equations
Substitute
Now that you have the equation for the specific circuit, you can re-sub in the equations
Using the equations above, we can substitute in the expanded values